## Slide 1
Making Water Safe & Emergency Toilets
Lincoln County
Health & Human Services
Dan Norton, Emergency Preparedness

## Slide 2: Making water safe
Methods:
  Filtration
  Distillation/ Evaporation
  Boiling
  Disinfection
Contaminants:
  Microorganisms
  Dirt
  Chemicals

## Slide 3: Filtration
Physical separation
Removes:
  Particulate matter
  Some microorganisms
Start with clear, clean, & running water if possible

## Slide 4: Distillation/ Evaporation
Remove water vapor & condense
Removes:
  Particulate matter
  Microorganisms
  Salt

## Slide 5: Boiling
Cooks any contaminants
Kills:
  Microorganisms
Leaves:
  Salt
  Sediment

## Slide 6: Disinfection
Iodine
Chlorine
Chemically kills microorganisms
Leaves:
  Salt
  Sediment
Bleach Use:
- 8 drops per gallon for clear water
- 16 drops per gallon for cloudy water
- Shake
- Let stand for 30+ minutes

## Slide 7
Emergency Toilet Options
Lincoln County
Health & Human Services
Septic system functional?
One bucket toilet available?
Two bucket toilets available?
Latrine/ Pit toilet
If yes, continue to use. If no, see below.
Use Twin bucket system
Use One bucket system
Talk to neighbors, grab a shovel
Storage or compost
Storage or compost
Determine location

## Slide 8: Sewage safety
Confirm septic or city sewer line intact: No puddles in yard, bad odor, visible sewage.
Toilet may flush but piping could be damaged
Understand issues/risks if composting
Store safely away from pets, kids, food, water, pests
Keep separate from regular garbage & yard debris
Do not bury sewage in plastic bags

## Slide 9: Two Bucket System
Poo Bucket:
  Reduce volume, slosh, contamination
  TP is ok
  Store or compost
Pee Bucket:
  Sterile, dilute & spread on lawn

## Slide 10: One Bucket System
Combined Bucket:
  Recommend double bagging waste
  Use carbon (sawdust, bark chips, pellets, cat litter, cut newspaper) to cover and reduce odor.
  Fill only 60% full
  Use care when moving
  Clean bucket as needed
  TP is ok
  Store or compost

## Slide 11: Latrine/ Pit toilet
Talk with neighbors, dig shared pit
Locate: 100+ ft from well or creek
Hole: 2-4 feet deep, 2 feet wide
Cover with handful of dirt after each use
Pit full if 1 ft left. Cover & dig new pit.

## Slide 12
Thank you!
Lincoln County
Health & Human Services